## Slide 1
Presentation of ABAQUS software
Principles and function
October, 2024
Hamza MECHAKRA
M’Hamed Bougara University of Boumerdes, Algeria
Dynamic Motors and Vibroacoustics Laboratory / DMVL

## Slide 2: Contact information and reference
Hamza MECHAKRA
Website: hamza-mechakra.webobo.com
Email: mechakra_h@univ-boumerdes.dz
Youtube: ABAQUS SIMULATION
References:
ABAQUS 6.13-1 documentation
www.simulia.com

## Slide 3: Summary
Subjects covered in this tutorial
An introduction to Abaqus / AbaqusCAE for beginners
A guided example to construct the finite element model of a simple structure
Comparison analytical vs numerical solutions
Other few exercises
Lab –course structure:
In each lesson one example will be presented and explained
At the end of each lesson, few exercises will be proposed in order to evaluate comprehension
For the final evaluation it’s necessary to produce the collection of the proposed exercises solved and discussed

## Slide 4
Abaqus is a suite of powerful engineering simulation programs, based on the finite element method, that can solve problems ranging from relatively simple linear analyses to the most challenging nonlinear simulations.
ABAQUS/CAE
Simulation of ABAQUS Software

## Slide 5
Figure.1 The Start Session dialog box.
Starting Session Abaqus/CAE

## Slide 6
Figure.2 Components of the main window.
Components of the main window
Notes: Figure.2 shows the components that appear in the main window. The components are:

## Slide 7
Title bar
The title bar indicates the release of Abaqus/CAE you are running and the name of the current model database.
Menu bar
The menu bar contains all the available menus; the menus give access to all the functionality in the product.
Toolbars
The toolbars provide quick access to items that are also available in the menus.
Context bar
Abaqus/CAE is divided into a set of modules, where each module allows you to work on one aspect of your model; the Module list in the context bar allows you to move between these modules
Components of the main window

## Slide 8
Model Tree
The Model Tree provides you with a graphical overview of your model and the objects that it contains, such as parts, materials, steps, loads, and output requests.
Results Tree
The Results Tree provides you with a graphical overview of your output databases and other sessionspecific data such as X–Y plots.
Toolbox area
When you enter a module, the toolbox area displays tools in the toolbox that are appropriate for that module.
Viewport
Viewports are windows on the canvas in which Abaqus/CAE displays your mode
Components of the main window

## Slide 9
Prompt area
The prompt area displays instructions for you to follow during a procedure; for example, it asks you to select the geometry as you create a set.
Message area
Abaqus/CAE prints status information and warnings in the message area.
Command line interface
You can use the command line interface to type Python commands and evaluate mathematical expressions using the Python interpreter that is built into Abaqus/CAE.
Components of the main window

## Slide 10
What is a module?
As mentioned earlier, Abaqus/CAE is divided into functional units called modules (fig-3) . Each module contains only those tools that are relevant to a specific portion of the modeling task
Figure.3 Selecting a module.

## Slide 11
Figure.4 Model Tree.
Model Tree

## Slide 12
Before starting to define any model, you need to decide which system of units you will use. ABAQUS has no built-in system of units.
Units
Quantity | SI | SI (mm)
Length | m | mm
Force | N | N
Mass | kg | tonne (103 kg)
Time | s | s
Stress | Pa (N/m2) | MPa (N/mm2)
Energy | J | mJ (10–3 J)
Density | kg/m3 | tonne/mm3

## Slide 13
Figure.3 Elements types .
Elements types

## Slide 14
Elements types names
B21 : Beam, 2-D, 1st order Interpolation
C3D20: Continuum, 3-D, 20-noded solid element
S8R : Shell, 8-node, Reduced Integration

## Slide 15
Elements types names
CPE8 : Continuum Plane Strain 8 noded
CPS8 : Continuum Plane Stress 8 noded

## Slide 16
Materials behavior

## Slide 17
Materials library

## Slide 18
Procedures
ABAQUS CAE
ABAQUS
ABAQUS
Viewer
cae
inp
log
dat
msg
odb
ps
ascii
database
Message file
Output database
Printed output
inp
Pre
Processing
Analysis
Post
Processing
Postscript Output
+ Other formats
Represents files which are identified by the extension name ” ......’’

## Slide 19
Elements types names

## Slide 20: AbaqusCAE structure
AbaqusCAE is divided into the following modules:
Part – Create individual parts (geometry)
Property – Create and assign material properties; for beam and bar elements it allows to create and assign the transversal section
Assembly – Create and place all parts in instances (assemblies): it allows to translate, to rotate, to duplicate each part
Step – Define all analysis steps and the results you want (output): the analysis may be static, dynamic, frequency
Interaction – Define any contact information or special constraints
Load – Define and place all loads (force, moment, pressure, body gravity,…) and boundary conditions (encastre, pin,…)
Mesh – Define nodes and elements of the discretized structure
Job – Create the input file for abaqus solver; submit directly the job for analysis (abaqus solver embedded)
Visualization – View your results

## Slide 21: Exercise 1 – Modeling geometry
Module Part
Sketch the part as 2D planar deformable wire
Note: in module part it’s possible to create 1D, 2D and 3D geometry as like as another CAD software
AbaqusCAE is not so powerful: if you want to create complex geometry, it’s better to use other CAD system (CATIA, ProE, SolidWorks,…) and import the model in AbaqusCAE

## Slide 22: Exercise 1 – Defining property
Module Property
Define material property
Create section with area A and material just defined
Assign the section defined to the relative segment of the structure

## Slide 23: Exercise 1 – Assembly and CSYS
Module Assembly
Assembly the part!! Even if there’s only one part it must be create an assembly (instance)
Assembly may be created as dependent (the mesh will be created on each part) or independent (the mesh will be created on the assembly-instance)
Create a new CSYS rectangular located in 3 and directed as segment 3 (use 3 point method)

## Slide 24: Exercise 1 – Step
Module Step
Create a step in which it’s defined the analysis type (static, dynamic, frequency)
For this ex: static, general

## Slide 25: Exercise 1 – Load and boundary
Module Load
Define the force in 2
Define boundary condition in 1, 2 and 3 (for bc_3 use local CSYS)

## Slide 26: Exercise 1 - Mesh
Module Mesh
Assign mesh type (solver standard-static, order linear, family truss)
Define mesh seed (partition of the edge): seed by size (assign dimension of element); seed by number (define number of elem. on the edge)
Create mesh of the part (automatic process)

## Slide 27: Exercise 1 - Job
Module Mesh
Write input file (launch the solver from external shell)
Data check (evaluate inp file – find error)
Submit: launch solver (write files in work directory: see .dat!)
Monitor: pop-up window with warnings, errors and process messages
Results: load the solution of the analysis (it brings you to module visualization)